## Slide 1
PCS3732 · PROCESSOR LABORATORY · GROUP D
Smart Lock over
Bluetooth Low Energy
Physical-button enrollment · HMAC-SHA256 challenge–response
One wire protocol. Three implementations. No shared key ever crosses the air twice.
Group D · Escola Politécnica, University of São Paulo · 2026
Raspberry Pi 3B+
Python · BlueZ · D-Bus
BLE peripheral — the lock
iOS 17
Swift · SwiftUI · CoreBluetooth
BLE central
Android 26+
Kotlin · Compose · BluetoothGatt
BLE central
Notes: TARGET 0:10 (running 0:10). Good morning. This is Group D's project: a door lock that opens from a phone over Bluetooth Low Energy. Three implementations, one protocol. Keep this short — go straight to slide 2.

## Slide 2
MOTIVATION
Three questions a phone-opened lock must answer
1
Who is asking?
The lock needs a per-device identity, not one key shared by everybody who ever had access.
2
Can they prove it?
Proof must be unforgeable and unrepeatable. Anything static that crosses the air can be captured and replayed.
3
How did they get access
in the first place?
If enrollment happens purely over the radio, anyone within range can attempt it.
The third question has no cryptographic answer. Trust has to enter the system through a channel the attacker is not on.
REQUIREMENTS WE SET
R1
No replay
A captured exchange is useless the second time
R2
Revocable
Per-device credentials, individually revoked
R3
Physical presence
Enrollment requires a button on the lock
R4
Auditable
Who opened what, when, and whether it worked
R5
One protocol
Identical on iOS and on Android
Notes: TARGET 0:55 (running 1:05). Walk the three questions quickly — the audience already believes the first two. SLOW DOWN on the amber line. This is the thesis of the project: trust has to enter through a channel the attacker is not on. That is why there is a physical button on the lock. Read the five requirements fast — they come back on the next slide and during the demo.

## Slide 3
PROPOSED SOLUTION
Each requirement maps to one mechanism
R3
Enrollment is approved by a physical button on the lock.
Nothing sent over the air can bypass it.
R2
On approval the lock generates 32 random bytes, unique to that phone.
Revoking one phone touches nobody else.
R1
Unlocking is a challenge–response.
The lock issues a fresh nonce; the phone proves it holds the secret. The secret never crosses the air again.
R4
Every operation lands in a SQLite access log.
Which never contains a secret, a nonce, or a MAC.
R5
One wire format, three implementations.
The peripheral has no platform-specific code.
WHO SPEAKS IT
Raspberry Pi 3B+
Python · BlueZ
D-Bus
BLE peripheral
iOS 17
Swift · SwiftUI
CoreBluetooth
BLE central
Android 26+
Kotlin · Compose
BluetoothGatt
BLE central
Identical UUIDs, identical JSON, identical HMAC — verified by unit tests, not by inspection.
Notes: TARGET 0:55 (running 2:00). This slide is the whole design in one screen. Go row by row, but do not linger — each mechanism gets its own detail later. The one to emphasise is R3 (highlighted): the physical button is what makes the rest of the scheme meaningful. The bottom line matters for the testing slide later: 'identical' is verified, not asserted.

## Slide 4
ARCHITECTURE · 1 OF 2
System view
iPhone
CoreBluetooth central
Android phone
BluetoothGatt central
BLE GATT
Raspberry Pi 3B+
BLE peripheral · BlueZ
1 GATT service
7 characteristics — read, write-with-response, notify
Single GLib event loop — button interrupts and the actuator timer
are marshalled back onto it, so service state is never touched
by two threads at once.
Buttons S4 / S5
approve · deny
Status LEDs
waiting · approved · denied · unlocked
Relay K1
actuator, auto re-lock after 5 s
SQLite
enrolled devices · access log
Custom 128-bit UUIDs
A1B2000x-5F6D-4C3E-9A2B-7E8F0D1C2B3A — the service UUID must be in the advertisement, or the phone never sees the lock.
Compact UTF-8 JSON
Binary fields in Base64. Every message carries "v":1 — a version mismatch is rejected by both ends.
Write with response
On all three writable characteristics: the phone must know a message landed before it waits for the notification.
Notes: TARGET 0:50 (running 2:50). Read the diagram left to right: two centrals, one peripheral, four things the peripheral drives. Worth saying out loud: the peripheral has no idea which phone platform it is talking to. Everything platform-specific lives in the two apps. The three facts at the bottom are the wire-level contract. Do not read them verbatim — point at 'write with response' and explain why: the phone has to know the message landed before it starts waiting for a notification.

## Slide 5
ARCHITECTURE · 2 OF 2
The protocol
Enrollment
trust entering through the physical channel
phone -> Access Request
<- state = pending
[ owner presses ALLOW ]
32 random bytes (os.urandom)
<- state = approved + secret
stored in iOS Keychain / Android Keystore
A queue, not a single slot — two phones asking at once are served in arrival order, so the owner always knows what they are approving.
The lock times out at 55 s, deliberately shorter than the app's 60 s, so the app receives an explicit timeout instead of guessing.
A repeated request replaces the phone's earlier one; a phone that disconnects before the decision leaves the queue.
Unlock
challenge–response, once per command
mac = HMAC-SHA256(secret,
"unlock" || 0x00 || deviceId || 0x00 || nonce)
16-byte nonce, 5 s TTL, single use — each new read invalidates the previous challenge.
The "unlock" context string binds the proof to the operation: a captured MAC is useless for anything else.
One successful authentication authorises exactly one unlock command, and only for the deviceId that authenticated.
Constant-time comparison. Three bad attempts trigger a 30 s lockout that survives reconnection.
Challenge and session state are held per connection, so two phones operating in parallel never interfere with each other.
Notes: TARGET 1:05 (running 3:55). LEFT — enrollment. Walk the sequence. The line that matters is the owner pressing ALLOW: that is the moment trust is created, and it cannot be reached over the radio. Mention the queue: with a single slot, two simultaneous requests mean the owner does not know which phone they just approved. RIGHT — unlock. Point at the formula. Two details to call out: the 'unlock' context string means a captured MAC cannot be reused for another operation, and the 0x00 separators stop two different field splits from producing the same message. Last bullet is the practical defence: the lockout survives reconnection, so an attacker cannot reset the counter by dropping the link.

## Slide 6
DEMONSTRATION
Live, on the bench
1
Lock is up
SmartLock-Sala advertising; the app lists it under Nearby.
2
R3
Enroll
Tap Request access. The yellow LED comes on. Press ALLOW (S4) on the board — the app stores the credential.
3
R1
Unlock
Tap Unlock. The relay clicks, the blue LED comes on, and the lock re-engages automatically after 5 s.
4
Deny path
A second phone requests access. Press DENY (S5) — the app shows the request refused.
5
R2
Revoke
python -m smartlock revoke <deviceId> — the same phone now gets denied.
6
R4
Audit
python -m smartlock log — who, when, what, result. No secret, no nonce, no MAC anywhere in it.
Every requirement from slide 2 is exercised live — nothing here is a recording.
Notes: TARGET 2:30 (running 6:25). THIS IS THE SLIDE THAT ALWAYS OVERRUNS — watch the clock. Leave this slide on screen and work the hardware. It doubles as the script. Order: 1 advertising, 2 enroll + ALLOW, 3 unlock, 4 deny with the second phone, 5 revoke from the shell, 6 the access log. Say the requirement tag out loud as you hit each one (R3, R1, R2, R4) — it ties the demo back to the motivation. IF THE RADIO MISBEHAVES: skip to steps 5 and 6, which run entirely on the Pi over SSH and need no BLE at all. Do not debug live — say what should have happened and move on.

## Slide 7
RESULTS · 1 OF 2
What works
3
implementations,
one wire format
7
GATT characteristics
on a single service
~7.8k
lines of code
Pi 2.5k · iOS 1.9k · Android 3.3k
VERIFIED END TO END
iOS and Android both enroll, unlock and get revoked against the same lock — with no platform-specific code in the peripheral.
A second unlock inside the open window restarts the timer instead of opening a second one, so open time stays bounded by the last valid command.
DEPLOYED, NOT JUST DEMONSTRATED
Runs as a systemd unit: starts at boot, restarts on failure, database created under UMask 0077.
The service re-locks on shutdown — a process that dies does not leave the door standing open.
ACCESS LOG — NO SECRET, NO NONCE, NO MAC
2026-08-10T21:14:03+00:00 enroll ok 3f9c1a7e-5b02-4d18-9a44-0c7e2b61d8f0
2026-08-10T21:14:22+00:00 auth ok 3f9c1a7e-5b02-4d18-9a44-0c7e2b61d8f0
2026-08-10T21:14:22+00:00 unlock ok 3f9c1a7e-5b02-4d18-9a44-0c7e2b61d8f0
2026-08-10T21:19:41+00:00 auth rate_limited 8b2d0a41-6c33-47ff-b1e5-9d40a3c7e112
Notes: TARGET 0:50 (running 7:15). The three numbers are there so nobody has to guess the size of the thing. Do not read them — they are already on the screen. Spend the time on the two claims that matter: the peripheral contains zero platform-specific code, and the lock cannot be left open by a crash or by a repeated unlock.

## Slide 8
RESULTS · 2 OF 2
How we tested
Raspberry Pi
6 protocol scenarios
unittest against a virtual clock — no BLE, no GPIO, no wall clock
Raspberry Pi
8 advertisement-fallback tests
a fake btmgmt exercising both failure paths
Android
37 unit tests
crypto, codec, state machine, FakeLockTransport
iOS
MockLockTransport
an executable specification of the peripheral, runs in the Simulator
THE ONE WE ARE PROUDEST OF
Android's crypto tests run against vectors generated by the Pi's own implementation.
If the two ever disagree about a single byte of the HMAC, a JVM unit test fails — before anyone touches a radio.
SCENARIOS COVERED
Expired nonce · replayed session · revoked device · denied enrollment · temporary lockout · restart preserves enrolled devices
Testing the peripheral without hardware was a design constraint, not luck: the rule layer imports neither D-Bus nor GPIO, so the entire protocol runs on a laptop.
Notes: TARGET 0:45 (running 8:00). Do not read the table. Point at it and give the two takeaways: 1) The dark box: the Android crypto tests use vectors the Pi generated. Cross-implementation agreement is checked by a test, not by two people reading two files. 2) The italic line at the bottom: we can test the whole protocol on a laptop because the rule layer has no D-Bus and no GPIO dependency. That was a deliberate constraint.

## Slide 9
DIFFICULTIES · 1 OF 2
The advertisement that wouldn't
The GATT service registered fine. The advertisement did not — and without it the iPhone never sees the lock at all.
TRACED WITH btmon
1
BlueZ 5.82 takes the extended-advertising path
Add Ext Adv Params (0x0054), then Add Ext Adv Data (0x0055).
2
Params succeeds. Data returns Invalid Parameters
For a payload of any size — including zero bytes. So it is not the packet.
3
The controller does not implement the feature
BCM4345C0 reports HCI version 9 (BT 5.0), but LE Features bit 12 — Extended Advertising — is zero.
ROOT CAUSE
LE: 3f 00 00 08 00 00 00 00
bluetoothd was insisting on a feature the silicon does not have.
RESOLUTION
Try the D-Bus path first; on failure, fall back to the legacy MGMT path.
btmgmt --index 0 add-adv
-u <service uuid> -c -g -n 1
It succeeds on the same controller at the same instant. GATT stays registered with bluetoothd — only the advertisement changes route, and the phone cannot tell.
Notes: TARGET 0:50 (running 8:50). This is the best debugging story in the project — tell it as a story, in three beats. Beat 1: the service registers, the advertisement does not, and the symptom is that the iPhone simply shows an empty list. Beat 2: btmon shows Add Ext Adv Data failing with Invalid Parameters for a payload of ANY size — including zero bytes. That is what rules out our own packet. Beat 3: the controller advertises Bluetooth 5.0 but has the Extended Advertising feature bit set to zero. BlueZ was using a code path the hardware does not support. Then the fix: fall back to the legacy path, which works on the same chip at the same moment.

## Slide 10
DIFFICULTIES · 2 OF 2
Three stacks, one protocol
THE PROBLEM
WHAT WE DID ABOUT IT
Default ATT MTU is 23 bytes
An approved enrollment message is about 140 bytes.
Request a 185-byte MTU on connect. If it is refused, refuse to write rather than let the stack truncate silently — never shorten the secret.
BlueZ broadcasts notifications
It cannot address a notification to one central; every subscriber receives it.
Every notified message carries the deviceId, and each app discards what is not its own.
Android drops concurrent GATT operations
Silently — while CoreBluetooth quietly queues them.
A mutex serialising every read, write and notify-subscribe on the Android transport.
One protocol costs far more in the transport layer than it does in the cryptography.
Notes: TARGET 0:35 (running 9:25). Do not read three rows out loud — pick the MTU one, which is the most concrete: the approved enrollment message is 140 bytes and the default MTU is 23, so it would arrive truncated. The rule we adopted is to refuse to send rather than shorten the secret. Then land the amber line: none of these are cryptography problems. Making one protocol run on three stacks costs far more in transport than in crypto.

## Slide 11
FINAL REMARKS · 1 OF 2
Known limitations
1
The secret is broadcast at enrollment
BlueZ cannot address a notification to a single central, so the approved message reaches every subscribed central. The window is narrow — an attacker must already be connected and subscribed while the owner presses the button — but it is real.
2
The secret is stored in plaintext on the lock
HMAC is symmetric: the lock needs the same bytes to recompute the proof, so storing a hash is not an option. The file is mode 0600 — but root on the Pi owns the credentials.
3
The lock is not authenticated to the phone
A rogue peripheral advertising the same UUID can collect access requests. It harvests no secrets, since only the lock ever issues them, but it can deny service and mislead the user.
4
Lockout is per connection, not per device
The failed-attempt counter is indexed by the central's BLE address. An attacker who randomises that address on every attempt walks around the lockout entirely.
Every one of these has a named fix on the next slide.
Notes: TARGET 0:35 (running 10:00). Be brisk and be honest. Naming your own weaknesses reads as competence, not as failure — and the next slide answers every one of them. If time is short, cover 1 and 2 properly and say that 3 and 4 are on the slide. Likely question: 'why not just hash the secret?' Answer: HMAC is symmetric, the lock needs the same bytes to recompute the proof. Asymmetric crypto is exactly the fix on the next slide.

## Slide 12
FINAL REMARKS · 2 OF 2
Future work
1
Asymmetric cryptography
The phone generates a keypair and sends only the public key. The lock never transmits, and never stores, a secret — closing limitations 1 and 2 at the root.
2
LE Secure Connections
Marking the characteristics encrypt-read / encrypt-write / encrypt-notify makes the link opaque to bystanders. Already implemented behind a flag; off by default because LE pairing slows bench iteration.
3
Signed device information
So the phone can verify it is talking to our lock, not to a peripheral advertising the same UUID.
4
Global rate limiting
A per-lock ceiling on attempts instead of a per-connection one, which address randomisation defeats.
5
Background operation
CoreBluetooth state restoration, so unlocking no longer requires the app in the foreground.
The cryptography was the textbook part. The engineering was making three very different Bluetooth stacks agree on it — and finding that the reference implementation of one of those stacks was itself the thing standing in the way.
Notes: TARGET 0:35 (running 10:35). Item 1 is the headline: moving to a keypair means the lock never transmits and never stores a secret, which closes the two most serious limitations at once. Say that clearly. Items 2 to 5 are a list — point, do not read. End on the closing line and stop talking. Do not add a summary after it. Thank the audience and open for questions.